## Slide 1
Oesophageal Function Tests in Children: pH and Impedance, High-Resolution Manometry and EndoFLIP
Andrey Ermak, MD
Rosen 2018 (NASPGHAN/ESPGHAN) · Wenzl 2012 (EURO-PIG) · Gyawali 2024 (Lyon 2.0) · Yadlapati 2021 (Chicago v4.0) · López-Alonso 2006 · Pilic 2011 · Cresi 2020 · Singendonk 2014 and 2017 · Carlson 2016 and 2021 · Hirano 2017 (AGA) · Menard-Katcher 2017 · Hoffmann 2022
Why infants have no normal values · impedance sees what pH cannot · SI versus SAP · adult manometry criteria over-call children · when FLIP adds value

## Slide 2
I
THE QUESTION OF THE DAY
THREE TESTS, THREE DIFFERENT QUESTIONS
Choosing the oesophageal function test starts with the question, not with the catheter
2
Rosen R, et al. JPGN 2018;66:516–54 · Yadlapati R, et al. Neurogastroenterol Motil 2021;33:e14058 · Hirano I, et al. Clin Gastroenterol Hepatol 2017;15:325–34
pH-impedance
▪ Is reflux there, how high, acid or not?
▪ Do symptoms follow the events?
▪ Not a test for infant reflux disease
High-resolution manometry
▪ Does the body contract?
▪ Does the junction relax?
▪ Chicago v4.0, built on adults
EndoFLIP
▪ How stiff is the wall?
▪ Does the junction open under distension?
▪ An adjunct, never alone
The bedside task
▪ Name the question first
▪ Know which cut-offs are adult
▪ Plan PPI status before the study
The main idea. None of these tests has validated paediatric normal values. Each is most useful for a narrow question: linking symptoms to reflux, finding a motility disorder in dysphagia, or measuring how the oesophagogastric junction opens.
The clinical stake. Applied loosely, the same studies label normal infant reflux as disease and label normal small children as having spasm or outflow obstruction.

## Slide 3
I
HOW IMPEDANCE WORKS
IMPEDANCE SEES THE BOLUS, PH SEES THE ACID
Multichannel intraluminal impedance with pH (MII-pH): what each sensor records
3
Rosen R, et al. JPGN 2018;66:516–54 · Pilic D, et al. J Pediatr 2011;158:650–4 · Wenzl TG, et al. JPGN 2012;55:230–4 · Gyawali CP, et al. Gut 2024;73:361–71
1 · Rings
Paired electrodes along the catheter measure resistance to a small alternating current
2 · Liquid bolus
Conducts well: impedance falls by more than 50% from baseline
3 · Direction
Distal-to-proximal fall marks reflux; proximal-to-distal marks a swallow
4 · pH sensor
Classifies each event: acid below pH 4, weakly acidic 4–7, weakly alkaline above 7
5 · Baseline
Nocturnal baseline impedance falls when the mucosa is damaged and leaky
What pH alone misses. Non-acid reflux makes up 45–89% of paediatric reflux episodes, according to the 2018 guideline; a pH probe cannot see any of it. Infants fed every few hours buffer the stomach for much of the day.
What impedance adds. Number of events, proximal extent, bolus clearance and a mucosal integrity signal; it does not measure volume and is read partly by eye.

## Slide 4
II
THE HEALTHY PRETERM INFANT
MOST INFANT REFLUX IS WEAKLY ACIDIC AND HIGH
Reflux type in 21 healthy preterm neonates studied at a median of 12 days, % of events
4
López-Alonso M, et al. Pediatrics 2006;118:e299–308 · Rosen R, et al. JPGN 2018;66:516–54
72.9%
Weakly acidic
25.4%
Acid
0%
Weakly alkaline
71 per day
Median reflux events per 24 hours in healthy, asymptomatic preterm infants.
90%
Of events reached the proximal oesophagus.
5.59%
Median acid exposure, with a range of 0.04% to 20.69%: one healthy infant above 20%.
The implication
An 'abnormal' event count or acid time in an infant may be physiology; a study cannot diagnose reflux disease on numbers alone.

## Slide 5
II
REFERENCE VALUES
NO NORMAL CHILDREN, ONLY NEGATIVE STUDIES
95th percentile of the reflux index (% time pH below 4) in 195 symptomatic children whose studies were judged negative
5
Cresi F, et al. J Neurogastroenterol Motil 2020;26:370–7 · Rosen R, et al. JPGN 2018;66:516–54 · Gyawali CP, et al. Gut 2024;73:361–71
Newborns
5.89%
Infants
4.69%
Children 1–16 years
2.48%
Adult Lyon 2.0, 'normal'
below 4%
Adult Lyon 2.0, conclusive
above 6%
Ethics
The 2018 guideline: no true paediatric normal values exist, because healthy children cannot be catheterised for research.
Impedance events
95th percentile 5.67, 4.88 and 4.40 events per hour in newborns, infants and children (Cresi).
Read with care
The authors call their cohort 'not exactly normal'; the adult Lyon thresholds were never derived in children.

## Slide 6
II
WORKING THRESHOLDS
WHICH NUMBERS YOU CAN USE, AND THEIR PEDIGREE
Paediatric working cut-offs against adult Lyon Consensus 2.0 (off PPI); always state which threshold the report used
6
Rosen R, et al. JPGN 2018 · Pilic D, et al. J Pediatr 2011 · Gyawali CP, et al. Gut 2024;73:361–71 · Pop RS, et al. J Clin Med 2024;13:3351
Metric | Paediatric working value | Adult Lyon 2.0 | Pedigree in children
Acid exposure (reflux index) | Abnormal above 10% under 1 year; above 5% over 1 year | Below 4% normal; above 6% conclusive | Quoted by the 2018 guideline; not validated
Reflux events per 24 h | Above 100 under 1 year; above 70 from 1 year | Below 40 against; above 80 supports | German multicentre working values
Mean nocturnal baseline impedance | One study: 1,466 Ω (AUC 0.73) | Below 1,500 Ω supports; above 2,500 Ω against | Insufficient
Symptom index | 50% or more positive | Above 50%: supportive only | No index preferred (2018)
Symptom association probability | 95% or more positive | Above 95%: supportive only | No outcome data
Post-reflux swallow index | No cut-off | Retired to research use | None

## Slide 7
III
WHAT IMPEDANCE ADDS
HALF OF ABNORMAL STUDIES ARE INVISIBLE TO PH
How 270 abnormal paediatric MII-pH studies were detected, German Pediatric Impedance Group, 700 children aged 3 weeks to 16 years
7
Pilic D, et al. J Pediatr 2011;158:650–4 · Rosen R, et al. JPGN 2018;66:516–54
Impedance only
45% (120)
Both
37% (101)
pH only
18% (49)
82%
Agreement between symptom index and symptom association probability (kappa 0.54): they disagree in about one study in five.
Infants
Had more reflux episodes than older children, as expected from feeding volume and posture.
Minimum
At least 18 hours of recording; an impedance event is a fall of more than 50% from baseline.
Caveat. 'Abnormal by impedance only' rests on event-count thresholds that are themselves unvalidated in children.

## Slide 8
III
SYMPTOM ASSOCIATION
LINKING THE COUGH TO THE REFLUX
Two indices, one underlying problem: symptom reporting in children
8
Wiener GJ, et al. Am J Gastroenterol 1988;83:358–61 · Weusten BL, et al. Gastroenterology 1994;107:1741–5 · Rosen R, et al. JPGN 2018 · Gyawali CP, et al. Gut 2024
Symptom index
▪ % of symptoms preceded by reflux
▪ Positive at 50% or more
▪ Ignores how many refluxes had no symptom
Association probability
▪ 2-minute segments, Fisher exact test
▪ SAP = (1 − P) × 100%; positive at 95%
▪ Disagreed with SI in 11% of 184 studies
The paediatric problem
▪ Parents miss over 50% of symptoms
▪ Cough and arching are non-specific
▪ No index predicts outcome (2018)
Adult performance
▪ SI: sensitivity 80%, specificity 35%
▪ SAP: sensitivity 73%, specificity 65%
▪ Lyon 2.0: supportive only
Use it for. A verbal child with a frequent, well-marked symptom, or an infant whose cough or apnoea can be logged by a nurse or a video; then a positive association is meaningful.
Do not use it for. Calling a fundoplication justified on a positive index alone, or dismissing reflux because a sleepy infant had too few marked symptoms.

## Slide 9
III
BEFORE FUNDOPLICATION
THE STUDY DOES NOT PREDICT THE OPERATION
Two paediatric surgical cohorts with conflicting answers
9
Rosen R, et al. JPGN 2010;50:251–5 · Mauritz FA, et al. Surg Endosc 2017;31:1101–10 · Rosen R, et al. JPGN 2018;66:516–54
P > 0.1
Rosen 2010, 34 children: no pre-operative MII-pH marker (acid, non-acid, total events) predicted symptom outcome
P > 0.4
A positive symptom index or symptom sensitivity index did not predict improvement either
8.5% → 0.8%
Mauritz 2017, 25 children: acid exposure after laparoscopic fundoplication; more pre-operative events, bigger fall
3 of 25
Developed new dysphagia; sphincter pressure rose from 10 to 24 mmHg
Reading the two. Fundoplication reliably lowers measured reflux; whether the symptom that prompted surgery goes away is a separate question the pre-operative study does not answer.
In practice. Use MII-pH to document that reflux is real and frequent, then make the surgical decision on the clinical picture, failed medical therapy and the family's goals.

## Slide 10
III
DOING THE STUDY
DECIDE ON OR OFF PPI BEFORE YOU PLACE THE CATHETER
Indications and practical protocol for MII-pH in children
10
Rosen R, et al. JPGN 2018;66:516–54 (rec. 3.17) · Wenzl TG, et al. JPGN 2012;55:230–4 · Cresi F, et al. JNM 2020 · Gyawali CP, et al. Gut 2024
1 · Indication
Correlate persistent troublesome symptoms with reflux; separate NERD, reflux hypersensitivity and functional heartburn
2 · PPI status
Off acid suppression to test whether reflux causes symptoms; on it to test whether therapy works
3 · Washout
About 7 days off PPI is common practice; no paediatric guideline specifies a number
4 · Record
About 24 hours, at least 18; meals, position and symptoms logged; wireless pH at least 48 hours
5 · Report
State age, PPI status, thresholds used and symptom indices with their caveats
Where it adds most (EURO-PIG). Symptoms on PPI, feeding-related symptoms and intermittent symptoms; its limits are cost, effect on decisions and the absence of evidence-based paediatric parameters.
Not a reason to test. Regurgitation in a thriving infant, or diagnosing reflux disease in an infant from numbers alone.

## Slide 11
IV
HIGH-RESOLUTION MANOMETRY
CHICAGO V4.0: THE METRICS THAT MAKE A DIAGNOSIS
Protocol and thresholds in Chicago Classification v4.0, derived in adults
11
Yadlapati R, et al. Neurogastroenterol Motil 2021;33:e14058 · Rosen R, et al. JPGN 2018;66:516–54
Element | Chicago v4.0 definition | What it tells you
Protocol | Supine: 10 wet 5 mL swallows plus multiple rapid swallows; upright: 5 swallows plus 200 mL rapid drink | Positional and provocative tests reduce false calls
Integrated relaxation pressure (IRP) | Upper limit supine 15 mmHg (Medtronic) or 22 mmHg (Laborie/Diversatek); upright 12 or 15 | Does the junction relax with a swallow?
Distal contractile integral (DCI) | Below 100 failed; 100 to 450 weak; above 8,000 hypercontractile | Vigour of the body contraction
Distal latency | Below 4.5 seconds with DCI 450 or more: premature | Loss of inhibition, as in spasm or type III achalasia
Pressurisation | Panoesophageal in 20% or more of swallows | Defines type II achalasia
Not for GERD. The 2018 paediatric guideline advises against manometry to diagnose reflux disease (rec. 3.9) and for it when a motility disorder is suspected (rec. 3.10).

## Slide 12
IV
DIAGNOSES
THREE ACHALASIAS AND TWO NEIGHBOURS
Chicago v4.0 categories that matter most in children with dysphagia
12
Yadlapati R, et al. Neurogastroenterol Motil 2021;33:e14058
Achalasia I
▪ High IRP
▪ 100% failed peristalsis
▪ No pressurisation
Achalasia II
▪ High IRP, 100% failed
▪ Panoesophageal pressure in 20% or more
▪ Best response to therapy
Achalasia III
▪ High IRP
▪ Premature contractions in 20% or more
▪ No normal peristalsis
Outflow obstruction
▪ High IRP supine and upright
▪ Plus symptoms and a supportive test
▪ Timed barium swallow or FLIP
Ineffective motility
▪ Over 70% ineffective or 50% failed
▪ 50–70%: inconclusive
▪ Fragmented now included
The v4.0 change that matters. Outflow obstruction is now conclusive only with relevant symptoms and a supportive test, because a raised IRP alone was over-called; distal spasm and hypercontractile oesophagus also need symptoms.
Why it matters more in children. Small oesophagi and short distances shift the very metrics these categories rest on.

## Slide 13
IV
CHILDREN ARE NOT SMALL ADULTS
ADULT CRITERIA OVER-CALL DISEASE IN CHILDREN
Children labelled with abnormal motility by Chicago criteria, standard versus adjusted, 76 children, mean age 9 years, %
13
Singendonk MMJ, et al. Neurogastroenterol Motil 2014;26:1333–41 (Chicago 2012 criteria)
Standard adult criteria
66%
Age-adjusted
50%
Size-adjusted
53%
13% → 7%
Outflow obstruction after age adjustment.
14% → 1%
Diffuse oesophageal spasm after age adjustment.
Why
Younger and smaller children had higher IRP and shorter distal latency, the two metrics that define obstruction and spasm.
No paediatric Chicago v4.0 consensus or validated paediatric normal values were found. Treat 'spasm' and 'outflow obstruction' in a small child as hypotheses.

## Slide 14
IV
PAEDIATRIC ACHALASIA
RARE, RISING, AND BEST READ BY AN EXPERT
What the paediatric data add
14
Marlais M, et al. Arch Dis Child 2011;96:192–4 · Singendonk MMJ, et al. Neurogastroenterol Motil 2017;29 · Peña-Vélez R, et al. Rev Esp Enferm Dig 2020;112:850–3
0.18 per 100,000
UK childhood achalasia incidence per year, 228 cases 1998–2008, rising (odds ratio 1.12 per year)
10.9 years
Mean age at diagnosis in the UK series; 56% boys
κ 0.52 → 0.92
Agreement on the diagnosis between six raters: software alone versus expert review
48%
Of 54 children with dysphagia studied by HRM had a motility disorder
Subtype is harder than diagnosis. Agreement on achalasia subtype rose only from 0.28 to 0.58 with expert override; the authors recommend paediatric motility centres for interpretation.
Think beyond achalasia. Ineffective motility was as common as achalasia among children with dysphagia; eosinophilic oesophagitis and repaired atresia are the usual backdrops.

## Slide 15
V
ENDOFLIP
MEASURING HOW THE JUNCTION OPENS
Functional lumen imaging probe: impedance planimetry during controlled balloon distension
15
Hirano I, et al. Clin Gastroenterol Hepatol 2017;15:325–34 · Carlson DA, et al. Am J Gastroenterol 2016;111:1726–35 and 2021;116 · Nguyen AD, et al. Gastroenterology 2025 (AGA update)
1 · Balloon
16 cm catheter placed across the junction at endoscopy; filled in steps of 30 to 60 mL
2 · Geometry
Impedance electrodes compute the diameter along the balloon
3 · Distensibility
Narrowest area divided by balloon pressure: the distensibility index (DI)
4 · Panometry
Repetitive contractions to distension show the body's response
5 · Read
Normal: DI 2.0 or more and diameter 16 mm or more; reduced: DI below 2.0 and diameter below 12 mm
95%
Carlson 2016: FLIP abnormal in 95% of adults with abnormal HRM, including all 70 with achalasia; also abnormal in 50% with normal HRM.
92%
Carlson 2021, 539 adults: reduced opening with absent or impaired response matched an outflow disorder in 92%.

## Slide 16
V
FLIP IN PAEDIATRIC EOE
A STIFF OESOPHAGUS PREDICTS THE IMPACTION
Median oesophageal distensibility index by phenotype, 59 patients aged 9–21 with eosinophilic oesophagitis, mm²/mmHg
16
Hoffmann NV, Keeley K, Wechsler JB. Clin Gastroenterol Hepatol 2022 · Menard-Katcher C, et al. Am J Gastroenterol 2017;112:1466–73
3.3
Fibrotic features
5.5
Inflammatory features
P = 0.02
Below 4.5
Distensibility index predicted grade 2 rings (area under the curve 0.81).
Odds ratio 1.44
Distensibility predicted food impaction after adjustment.
No correlation
With eosinophil count: stiffness and inflammation are separate axes.
Menard-Katcher 2017
88 children with EoE versus 44 controls: distensibility rises with age and is lower in EoE, more so with fibrosis and strictures.

## Slide 17
V
WHEN FLIP IS NEEDED
FOUR QUESTIONS FLIP ANSWERS BETTER
Indications in children, and the limits
17
Yadlapati 2021 · Hirano 2017 · AGA statements · Destro F, et al. Children 2022;9:1426 · White E, Mutalib M. World J Clin Pediatr 2023;12:162–70
Outflow obstruction
▪ Chicago v4.0 supportive test
▪ Confirms or refutes a high IRP
▪ Alternative: timed barium swallow
Achalasia treatment
▪ Measured at dilation or myotomy
▪ Post-treatment DI below 2–3 suggests incomplete
▪ Guides the next step
EoE remodelling
▪ Severity and stricture risk
▪ Monitors therapy
▪ Never diagnoses EoE
After surgery
▪ Fundoplication or atresia dysphagia
▪ Atresia series: median EGJ DI 2.58
▪ Tight wrap versus dysmotility
The limits. No paediatric FLIP normal values exist and the effect of sedation or anaesthesia has not been studied; the AGA advises never to base a decision on FLIP alone and not to use it routinely for reflux.

## Slide 18
VI
CHOOSING THE TEST
MATCH THE QUESTION TO THE TOOL
A practical sequence for the child referred for oesophageal testing
18
Rosen 2018 · Wenzl 2012 · Yadlapati 2021 · Hirano 2017 · Singendonk 2014
Clinical question | First test | Then, if needed
Are symptoms on PPI still caused by reflux? | MII-pH on PPI | Endoscopy if not done; consider hypersensitivity
Is the non-verbal child's cough or apnoea linked to reflux? | MII-pH off PPI with nurse or video marking | Treat the association, not the event count
Dysphagia with normal endoscopy and biopsies | HRM | Timed barium swallow or FLIP if IRP is high
HRM shows outflow obstruction | FLIP or timed barium swallow | Repeat or reinterpret against paediatric data
EoE with impaction or narrowing | Endoscopy with FLIP | Dilation; track distensibility on therapy
Before fundoplication | MII-pH to confirm reflux | HRM if dysphagia or motility disorder is suspected

## Slide 19
VII
GUIDELINES
WHAT THE DOCUMENTS SAY
North America (NASPGHAN/ESPGHAN joint 2018, AGA) versus Europe and international (EURO-PIG, BSPGHAN, Lyon 2.0, Chicago v4.0)
19
Rosen 2018 · Wenzl 2012 · Mutalib 2017 (BSPGHAN) · Gyawali 2024 (Lyon 2.0) · Yadlapati 2021 · Hirano 2017 and Nguyen 2025 (AGA)
Question | North America | Europe and international | Verdict
Role of MII-pH | Joint 2018: correlate symptoms; define NERD | EURO-PIG, BSPGHAN: test of choice; best on PPI | ALIGNED
Paediatric normal values | Joint 2018: none exist | BSPGHAN and EURO-PIG: none exist | ALIGNED
Symptom indices | Joint 2018: no index preferred | Lyon 2.0 (adult): supportive only | ALIGNED
Acid exposure cut-off | Joint 2018 quotes above 10% (infant), 5% | Lyon 2.0 adult: below 4%, above 6% | DIFFERS
Manometry classification | No paediatric criteria | Chicago v4.0 adult; children over-called | MATERIAL
FLIP | AGA: adjunct only, adult | No ESPGHAN statement; no paediatric norms | GAP
Material gap: adult Chicago v4.0 thresholds applied to a small child can manufacture spasm or outflow obstruction.

## Slide 20
VIII
TRAPS
WHERE OESOPHAGEAL TESTING MISLEADS
Common reasons for a wrong answer
20
López-Alonso 2006 · Rosen 2010 and 2018 · Singendonk 2014 · Hirano 2017
"Abnormal pH study"
▪ Healthy infants reflux 70 times a day
▪ Up to 20% acid time in one
▪ Ask: abnormal for what age?
"SI positive, operate"
▪ No index predicts outcome
▪ Fundoplication fixes numbers
▪ Decide on the clinical picture
"Spasm on HRM"
▪ Short latency in small children
▪ 14% falls to 1% when adjusted
▪ Expert paediatric read
"FLIP says EoE"
▪ FLIP measures stiffness
▪ Biopsies diagnose EoE
▪ Never decide on FLIP alone
Every number in an oesophageal report should carry its age, its PPI status and the population it came from.

## Slide 21
VIII
PEARLS
EIGHT THINGS TO REMEMBER
The numbers worth carrying into clinic
21
López-Alonso 2006 · Rosen 2018 · Pilic 2011 · Cresi 2020 · Gyawali 2024 · Yadlapati 2021 · Singendonk 2014 · Hoffmann 2022
▪ Healthy preterm infants: about 71 reflux events a day, 73% weakly acidic, 90% reaching the proximal oesophagus.
▪ Non-acid reflux is 45–89% of paediatric episodes; pH alone misses it.
▪ In 270 abnormal paediatric studies, 45% were abnormal by impedance only.
▪ There are no true paediatric normal values; adult Lyon 2.0 says AET below 4% normal, above 6% conclusive.
▪ SI (50%) and SAP (95%) agree in about four of five studies; no index predicts surgical outcome.
▪ Chicago v4.0: outflow obstruction needs symptoms plus a supportive test; IRP limits are device-specific.
▪ Adult criteria label 66% of children abnormal; 50% after age adjustment; spasm 14% to 1%.
▪ FLIP: normal EGJ-DI 2.0 or more; in paediatric EoE a DI below 4.5 flags rings and impaction risk.

## Slide 22
VIII
SYNTHESIS — SCENARIO TO PLAN
FROM SCENARIO TO DECISION
Applying the logic in the motility clinic
22
Rosen 2018 · Yadlapati 2021 · Singendonk 2014 · Hoffmann 2022 · Hirano 2017
Scenario | Think | Do now
3-month-old, regurgitation, thriving, 'abnormal' pH study | Physiological reflux | No treatment escalation; reassure; no repeat study
12-year-old, heartburn despite PPI, normal endoscopy | Reflux hypersensitivity or functional | MII-pH on PPI; symptom association with caveats
6-year-old, HRM reads 'diffuse spasm' | Adult criteria in a small child | Expert paediatric re-read; age-adjusted interpretation
14-year-old, dysphagia, IRP high, peristalsis present | Possible outflow obstruction | FLIP or timed barium swallow before treating
Teenager with EoE and two impactions | Fibrostenotic remodelling | Endoscopy with FLIP; dilate; track DI on therapy

## Slide 23
Oesophageal Function Tests in Children: pH and Impedance, High-Resolution Manometry and EndoFLIP
Andrey Ermak, MD