## Slide 1
Elastography in the Child's Liver
Andrey Ermak, MD
WFUMB 2024 · AASLD 2024 imaging NILDA · SRU 2020 · EASL 2021 · Baveno VII · AASLD 2025 · ESPGHAN 2026
TE · pSWE · 2D-SWE · MRE · CAP · paediatric norms · false stiffness

## Slide 2
I
THE MACHINES
FOUR WAYS TO MEASURE STIFFNESS
Method | How the shear wave is made | What is sampled | Reported as | Paediatric catch
VCTE (FibroScan) | Mechanical punch from the probe tip; no B-mode image | A blind cylinder ≈ 1 × 4 cm, 25–65 mm deep (M probe) | kPa (Young's modulus); CAP in dB/m | Probe by thorax: S1 < 45 cm, S2 45–75 cm, M > 75 cm
pSWE (ARFI) | Acoustic push at one point, under B-mode | One small ROI 15–20 mm below the capsule | m/s or kPa, vendor-specific | Short breath-hold needed; few child norms per vendor
2D-SWE | Repeated pushes building a colour map | ROI ≥ 10 mm chosen on the live image; 3–5 readings | kPa or m/s, vendor-specific | Works in neonates; long cine-loop in free breathing
MR elastography | 60 Hz passive driver on the abdomen | Large slices of the whole liver | kPa of shear stiffness (≈ one-third of the US scale) | Needs a still child — sedation below school age
CAP (on VCTE) | Attenuation of the same ultrasound signal | The VCTE cylinder | dB/m | Not validated against histology in most paediatric cohorts
2
Sterling RK, et al. Hepatology 2025;81:672–724 · Ferraioli G, et al. Ultrasound Med Biol 2024;50:1071–87 · Engelmann G, et al. Eur J Pediatr 2012;171:353–60 · Barr RG, et al. Radiology 2020;296:263–74

## Slide 3
I
THE MACHINES
WHAT MAKES A READING VALID
Every adult acquisition rule bends in a child; some break
Adult rule | What happens in children | Verdict
Fast 4 h; rest 10 min | Infants cannot fast — scan just before the next feed; stiffness rises for ~60 min after a meal | DIFFERS
Breath-hold in neutral expiration | Free breathing reads 11.1% lower than breath-hold on 2D-SWE | DIFFERS
≥ 10 valid VCTE shots, IQR/M ≤ 30% | Same rule; invalid exams cluster in younger children (mean 5.8 vs 9.7 y) | ALIGNED
No sedation | Sedation independently raises stiffness in the paediatric IPD meta-analysis | PAEDS ONLY
M or XL probe by skin–capsule distance | S1/S2 probe below 75 cm thorax; S-probe use raised stiffness in the IPD | PAEDS ONLY
Change > 10% is real (WFUMB, same machine) | Inter-observer limits of agreement in children: ± 31.8% of the mean | CONTRADICT
3
Ferraioli G, et al. Ultrasound Med Biol 2024;50:1071–87 · Mederacke I, et al. Liver Int 2009;29:1500–6 · Yoon HM, et al. Eur J Radiol 2017;97:53–8 · Engelmann G, et al. Eur J Pediatr 2012;171:353–60 · Li DK, et al. Liver Int 2020;40:2602–11

## Slide 4
II
NORMAL
NORMAL RISES WITH AGE
Transient elastography in healthy children, kPa
4.4
6.0
3.4
4.6
0–5 years
4.7
6.7
3.8
6.1
6–11 years
5.1
6.8
4.1
7.9
12–18 years
Median, Heidelberg
ULN, Heidelberg
Median, Osaka
95th pct, Osaka
kPa
IPD meta-analysis, 652 healthy children: reference range 2.45–5.56 kPa.
Age, sedation, S-probe use and steatosis on ultrasound all push the value up.
4
Engelmann G, et al. Eur J Pediatr 2012;171:353–60 · Tokuhara D, et al. PLoS One 2016;11:e0166683 · Li DK, et al. Liver Int 2020;40:2602–11

## Slide 5
II
NORMAL
NORMAL DEPENDS ON THE MACHINE
The same healthy liver gives a different number on each platform
5.56 kPa
Upper limit of normal VCTE across 10 studies, 652 children (IPD)
3.3 vs 4.1
Median kPa, 2D-SWE vs pSWE and VCTE, same 4–17-year-olds
6.0 kPa
Newborn median on Canon 2D-SWE — falls towards 5.3 by adolescence
2.45 kPa
MRE mean in healthy 8–17-year-olds; 95th centile 3.19, above adults
A paediatric report must name the method, the probe and the vendor.
Up to 26% of carefully screened healthy children had an MRE value suggesting fibrosis by published thresholds.
5
Li DK, et al. Liver Int 2020;40:2602–11 · Mjelle AB, et al. JPGN 2019;68:706–12 · Charlier C, et al. Arch Pediatr 2025;32:322–8 · Sawh MC, et al. J Magn Reson Imaging 2020;51:919–27

## Slide 6
III
FALSE STIFFNESS
STIFF IS NOT ALWAYS SCARRED
Confounder | Evidence | Where it bites in children
Necro-inflammation | At the ALT peak every one of 18 adults with acute hepatitis read above cirrhosis cut-offs | AIH at onset, acute Wilson, viral hepatitis, rejection
Extrahepatic cholestasis | Biliary drainage: 15.2 → 7.1 kPa in 3–12 days; pig bile-duct ligation 4.6 → 8.8 kPa in 2 h | Biliary atresia, choledochal malformation, stones
Venous congestion | Clamped IVC: 3.1 → 27.8 kPa; reversed within 5 min of release | Fontan, right-heart failure, restrictive cardiomyopathy, SOS
Food | Rise for up to 60 min; 39% of normal livers crossed 6 kPa after breakfast | Infants fed on demand
Infiltration | Amyloid, tumour or storage cells stiffen the parenchyma | HLH, storage disease, leukaemic infiltration
Steatosis | Moderate-to-severe fat makes VCTE overestimate fibrosis | Adolescent MASLD
Ascites, obesity | Cause failure more than false values; VCTE worst, MRE least affected | Decompensated cirrhosis, severe obesity
6
Arena U, et al. Hepatology 2008;47:380–4 · Millonig G, et al. Hepatology 2008;48:1718–23 · Millonig G, et al. J Hepatol 2010;52:206–10 · Mederacke I, et al. Liver Int 2009;29:1500–6 · Sterling RK, et al. Hepatology 2025;81:672–724

## Slide 7
III
FALSE STIFFNESS
HOW HIGH WITHOUT CIRRHOSIS
Liver stiffness, kPa (VCTE); red = before, amber = after the cause was removed
Decompensated heart failure
40.7 kPa
…same patients, recompensated
17.8 kPa
Pig, inferior vena cava clamped
27.8 kPa
Pig, baseline
3.1 kPa
Fontan children, median 13.7 y
18.6 kPa
Matched healthy controls
4.7 kPa
Malignant biliary obstruction
15.2 kPa
…3–12 days after drainage
7.1 kPa
Every red bar sits above the 15 kPa that rules in advanced disease.
Measure after drainage, decongestion or the ALT has settled — or do not interpret.
7
Millonig G, et al. J Hepatol 2010;52:206–10 · Chen B, et al. Can J Gastroenterol Hepatol 2016;2016:7125193 · Millonig G, et al. Hepatology 2008;48:1718–23

## Slide 8
III
FALSE STIFFNESS
ALT AND THE CHILD
Inflammation inflates the low end, where most children sit
18 / 18
Adults with acute viral hepatitis above cirrhosis cut-offs at the ALT peak
154
Children and young adults with VCTE within 1 year of biopsy (Boston)
F0–F2
High ALT pushed LSM above 8.6 kPa — into the advanced-fibrosis range
F3–F4
No association between ALT and LSM once fibrosis was advanced
Repeat once ALT is below 2 × ULN before calling fibrosis in a mild case.
A very high value in a known cirrhotic is still cirrhosis; a high value in a child with ALT 600 is not yet anything.
8
Arena U, et al. Hepatology 2008;47:380–4 · Raizner A, et al. JPGN 2017;64:512–7 · Ferraioli G, et al. Ultrasound Med Biol 2024;50:1071–87

## Slide 9
IV
CUT-OFFS
THE ADULT RULES OF FOUR AND FIVE
WFUMB 2024: the rule of four "cannot be applied to the paediatric population"
Meaning in adults | VCTE — rule of 5 (Baveno VII) | ARFI-SWE — rule of 4 (SRU) | In a child
Normal | < 5 kPa (AASLD 2024) | ≤ 5 kPa (1.3 m/s) | ALIGNED
Rules out compensated advanced CLD | < 10 kPa | < 9 kPa (1.7 m/s) | ADULT ONLY
Suggestive; needs confirmation | 10–15 kPa | 9–13 kPa | ADULT ONLY
Rules in compensated advanced CLD | > 15 kPa | > 13 kPa (2.1 m/s) | DIFFERS
Suggests CSPH | 15–20 kPa with platelets < 110 | > 17 kPa (2.4 m/s) | NO DATA
Rules in CSPH | > 25 kPa | > 21 kPa (2.6 m/s) | NO DATA
Skip screening endoscopy | < 20 kPa and platelets ≥ 150 | — | DIFFERS
9
Ferraioli G, et al. Ultrasound Med Biol 2024;50:1071–87 · Barr RG, et al. Radiology 2020;296:263–74 · Ling YC, et al. JPGN 2024;79:222–8

## Slide 10
IV
GUIDELINES
WHAT THE DOCUMENTS SAY
Question | AASLD 2024 imaging NILDA | WFUMB 2024 (with SRU 2020) | Verdict
Paediatric cut-offs? | Disease-specific thresholds differ from adults; none endorsed | None can be recommended (LoE 2a, GoR B) — but ≤ 5 kPa rules out, ≥ 15 kPa rules in, except BA, CFLD, Fontan | EU ADDS
Which method in a child? | Insufficient evidence to prefer one (ungraded) | SWE helpful for diagnosis and follow-up | ALIGNED
Confounders named | Oedema, extrahepatic cholestasis, venous congestion; fasting and sedation | Congestion, obstructive cholestasis, inflammation | ALIGNED
Follow-up | Not a standalone test of regression or progression (ungraded) | Same machine and probe; change > 10% is meaningful | DIFFERS
Biliary atresia | Profound extrahepatic cholestasis lessens accuracy | Useful to separate BA from other cholestasis (AUC 0.91) | DIFFERS
Fontan | Congestion raises LSM independent of fibrosis | No thresholds; follow the trend from the child's own baseline | ALIGNED
10
Sterling RK, et al. Hepatology 2025;81:672–724 · Ferraioli G, et al. Ultrasound Med Biol 2024;50:1071–87 · Barr RG, et al. Radiology 2020;296:263–74

## Slide 11
V
BILIARY ATRESIA
STIFFNESS BEFORE KASAI
It ranks the risk; it does not replace the cholangiogram
83 / 79%
Pooled sensitivity / specificity for BA, 11 studies, 1,307 infants
> 1.84 m/s
2D-SWE: 92% sensitive, 79% specific in 41 prospective infants
13.0 kPa
2D-SWE cut-off for ≥ F3 in 216 infants; NPV 96%
17.5 kPa
Pre-Kasai F3–F4 in 33 infants: 64% sensitive, 86% specific
One in five non-BA infants reads as stiff: cholestasis itself raises the number.
Use it to move an infant up the queue, never to delay biopsy or intraoperative cholangiography.
11
Wagner ES, et al. World J Gastroenterol 2022;28:4726–40 · Dillman JR, et al. J Pediatr 2019;212:60–5 · Chen H, et al. Korean J Radiol 2021;22:959–69 · Yoon H, et al. Korean J Radiol 2023;24:465–75

## Slide 12
V
BILIARY ATRESIA
VARICES AFTER KASAI
Detection of oesophageal or gastric varices by VCTE, %
84
77
Liver ≥ 12.7 kPa (n = 73)
80
70
Liver ≥ 12.5 kPa (n = 51)
75
87
Spleen ≥ 28.9 kPa (n = 51)
85
76
Pooled liver (9 studies)
Sensitivity
Specificity
%
Baveno VII missed no varix needing treatment in 48 BA children (Taiwan); spleen stiffness ≥ 27.6 kPa predicted CSV in 150 Indian children.
No child bled with spleen stiffness below 60 kPa in Hannover — the spleen beats the liver here.
12
Chongsrisawat V, et al. BMC Gastroenterol 2011;11:41 · Sintusek P, et al. JPGN 2019;69:411–5 · Wagner ES, et al. World J Gastroenterol 2022;28:4726–40 · Ling YC, et al. JPGN 2024;79:222–8 · Goldschmidt I, et al. JPGN 2014;59:197–203

## Slide 13
V
BY DISEASE
WHERE IT WORKS, WHERE IT MISLEADS
Disease | Best paediatric evidence | Number to remember | Verdict
Cystic fibrosis | 160 children, dual-pass biopsy; LSM r = 0.67 with stage | 5.55 kPa flags CFLD (AUROC 0.82); 8.7 kPa F3–F4 (spec 100%); with APRI PPV 92% | USE
Biliary atresia, post-Kasai | Pooled 9 studies; F4 vs F0–F3 DOR 70 | Sensitivity 96%, specificity 89% for cirrhosis | USE
After liver transplant | 94 recipients, Boston | AUROC 0.71 for ≥ F2 at 6.5 kPa | WEAK
Fontan circulation | Fibrosis is universal by adolescence | VCTE 18.6 vs 4.7 kPa in controls; MRE mean 4.4 kPa in 206 patients | TREND ONLY
Treated AIH, PSC, storage | Adult and mixed data; no obstruction | ≈ 8 kPa suggests advanced disease (WFUMB, GoR C) | TREND ONLY
MASLD | Meta-analysis vs prospective NASH CRN | AUROC 0.96 vs 0.67 for advanced fibrosis | CONTRADICT
13
Lewindon PJ, et al. Clin Gastroenterol Hepatol 2019;17:2561–9 · Lam S, et al. J Can Assoc Gastroenterol 2019;2:71–80 · Wagner ES, et al. World J Gastroenterol 2022;28:4726–40 · Lee CK, et al. Pediatr Transplant 2020;24:e13736 · Chen B, et al. Can J Gastroenterol Hepatol 2016;2016:7125193 · Razavi J, et al. Pediatr Radiol 2025;55:2601–10 · Nichols LB, et al. JPGN 2026;82:741–50

## Slide 14
V
MASLD
META-ANALYSIS VS NASH CRN
VCTE for advanced fibrosis (F3–F4) in paediatric MASLD, %
89
67
Sensitivity
93
76
Specificity
96
67
AUROC × 100
Dong 2022 — 7 studies, 436 children
Nichols 2026 — NASH CRN, 92 children
%
Prospective, multicentre, biopsy within 6 months: PPV 40%, NPV 90% — a rule-out test at best.
ESPGHAN 2026: < 5.5 kPa excludes, > 10 kPa suggests advanced disease; AASLD 2025: adult thresholds not validated.
14
Dong B, et al. J Paediatr Child Health 2022;58:481–90 · Nichols LB, et al. JPGN 2026;82:741–50 · Xanthakos SA, et al. Hepatology 2025;82:1352–94 · Mann JP, et al. JPGN 2026;83:555–76

## Slide 15
VI
STEATOSIS
CAP IN CHILDREN
It separates fat from no fat; it cannot grade it
198 vs 290
Mean CAP dB/m, no steatosis vs steatosis on biopsy (n = 69)
0.80 vs 0.68
AUROC, CAP vs scored B-mode US for ≥ S1 in severe obesity — NS
310–325
Median CAP dB/m across steatosis grades 1–3 in NASH CRN: flat
183 dB/m
Median CAP in healthy children 1–18 y; not age-dependent
AASLD 2025: do not use CAP diagnostically. ESPGHAN 2026: adjunct, > 280 dB/m. AASLD 2024 adult threshold: 275.
MRI-PDFF remains the only paediatric fat measure with histological grading behind it.
15
Desai NK, et al. J Pediatr 2016;173:160–4 · Runge JH, et al. Eur Radiol 2021;31:1588–96 · Nichols LB, et al. JPGN 2026;82:741–50 · Tokuhara D, et al. PLoS One 2016;11:e0166683

## Slide 16
VI
MR ELASTOGRAPHY
THE MOST ACCURATE, THE HARDEST
Shear stiffness of the whole liver — at the price of a scanner and often sedation
2.45 kPa
Healthy 8–17-year-olds; higher than healthy adults (2.10)
88.9%
Accuracy for advanced fibrosis, 90 children with MASLD
72.2%
Accuracy for any fibrosis — early stages still blur
R2* > 76
s⁻¹ at 1.5 T: iron overload makes GRE-MRE fail
MRE kPa is shear stiffness; ultrasound kPa is Young's modulus — never compare across platforms.
Use it when you already need an MRI, or when ultrasound fails: obesity, ascites, a narrow intercostal window.
16
Sawh MC, et al. J Magn Reson Imaging 2020;51:919–27 · Schwimmer JB, et al. Hepatology 2017;66:1474–85 · Sterling RK, et al. Hepatology 2025;81:672–724

## Slide 17
VII
GUIDELINES
NORTH AMERICA VS EUROPE
Topic | North America | Europe | Verdict
Paediatric fibrosis thresholds | AASLD 2024: none; no preferred method | WFUMB 2024: none — yet ≤ 5 / ≥ 15 kPa offered | EU ADDS
Paediatric MASLD — VCTE | AASLD 2025: adult thresholds not validated | ESPGHAN 2026: < 5.5 excludes, > 10 suggests advanced | MATERIAL
Paediatric MASLD — CAP | AASLD 2025: not a diagnostic tool | ESPGHAN 2026: adjunct, > 280 dB/m | DIFFERS
Paediatric MASLD — MRE | Most validated for advanced fibrosis | Useful; cut-offs need validation | ALIGNED
Confounders | Congestion, cholestasis, oedema, ALT, food, sedation | Congestion, cholestasis, inflammation, food | ALIGNED
Serial measurements | Not standalone for regression or progression | > 10% change on the same machine | DIFFERS
Varices in children | Baveno VII is adult; no paediatric rule | No paediatric rule | NO DATA
17
Sterling 2025 · Xanthakos 2025 · Ferraioli 2024 · Mann 2026 · Barr 2020 · Ling 2024

## Slide 18
VII
PEARLS
EIGHT THINGS TO REMEMBER
▪ Normal VCTE in a child is below about 5.5 kPa; it rises with age, sedation, S-probe use and fat.
▪ Each platform has its own normal — 2D-SWE reads lower than pSWE and VCTE in the same child.
▪ Inflammation, cholestasis and congestion each push a non-cirrhotic liver past 15 kPa.
▪ In BA, stiffness ranks the infant; the cholangiogram decides.
▪ After Kasai, spleen stiffness predicts varices better than liver stiffness.
▪ In Fontan, read the trend from the child's own baseline, never the absolute number.
▪ Paediatric MASLD: VCTE is a rule-out test (NPV 90%, PPV 40%); CAP cannot grade fat.
▪ MRE kPa and ultrasound kPa live on different scales; never compare them.
18
Li DK, et al. Liver Int 2020;40:2602–11 · Mjelle AB, et al. JPGN 2019;68:706–12 · Millonig G, et al. J Hepatol 2010;52:206–10 · Wagner ES, et al. World J Gastroenterol 2022;28:4726–40 · Sintusek P, et al. JPGN 2019;69:411–5 · Nichols LB, et al. JPGN 2026;82:741–50

## Slide 19
VII
SYNTHESIS — SCENARIO TO READING
Scenario | What to do | How to read it | What not to do
Cholestatic infant, possible BA | 2D-SWE with the fasting US | High value raises urgency | Delay the cholangiogram on a low value
AIH or hepatitis at onset, ALT in hundreds | Wait for ALT < 2 × ULN | Then stage | Call cirrhosis at presentation
BA after Kasai, surveillance | VCTE plus spleen stiffness yearly | Rising trend, spleen > 28 kPa → endoscopy | Use adult rule of five alone
Fontan teenager | Same machine every visit | Change from own baseline | Stage from one value
Obese teen, raised ALT | VCTE after ALT confirmed | < 5.5 kPa reassures | Grade fat with CAP
Child with CF | VCTE plus APRI | ≥ 5.5–6 kPa with APRI → CFLD likely | Rely on LSM alone
Graft check after LT | VCTE with ALT and Doppler | Low value reassures weakly | Skip the protocol biopsy
Ultrasound fails or MRI needed anyway | MRE | Shear-stiffness scale | Compare with ultrasound kPa
19
Ferraioli 2024 · Sterling 2025 · Raizner 2017 · Wagner 2022 · Sintusek 2019 · Lewindon 2019 · Lee 2020 · Nichols 2026

## Slide 20
Elastography in the Child's Liver
Andrey Ermak, MD